## Slide 1
Principles of Architecture & Construction
  My Room Floor Plan

## Slide 3: Floor Plans
  A scale drawing of a horizontal section through a building at a given level
  This means that if we were to look directly straight down on a house, take a “cut” horizontally right through the house, then remove the top, what is left over would create a floor plan
  This would be like taking a piece of fruit and slicing it in half, then looking into one half

## Slide 4: Importance of Floor Plans
  The floor plan is the “heart” of a set of drawings
  There are many types of drawings that are used to build a house, but if you could only have one, the floor plan would be the one
  It is the most important because it can contain the most information of all the drawings
  Depending on size and space, the floor plan can contain many other notes and charts of information
  A properly created floor plan is a very valuable tool

## Slide 5: Creating Floor Plans
  It is important to always take note of permanent structures in a room
  These can be used as reference points
  There are three main elements in floor plans; walls, doors and windows
  These are usually permanent stationary structures, so they are good references
  Floor plans are interesting because you are taking vertical elements and trying to represent them horizontally
  This is usually in a fashion that you are not use to seeing or probably have never seen

## Slide 6: Creating Floor Plans - Scale
  Scale refers to the size of the actual drawing geometry
  The scale is in reference to an actual size in real life, ex. ¼” on paper is equal to 1’ in real life
  Scale enables use to take something very large and proportionately represent it on a small media, or vice versa, take something really small and represent it large
  Scale is sometimes a difficult concept to understand and master, but with practice it can become very simple to understand

## Slide 7: Creating Floor Plans - Walls
  The most important feature of a floor plan are the walls
  What is important to note, walls are always two parallel lines or maybe a poché or thick solid line
  Always start with the outside walls to create a solid foundation
  Interior walls would be placed next
  Exterior walls are usually represented a little thicker than interior walls, as they usually contain more materials to actually build them
  A good rule of thumb, 6” exterior walls, 4” interior walls

## Slide 8: Creating Floor Plans - Doors
  Doors are the next important, because you may not always have a window, but you always have to have at least one door
  Doors are good reference because most standard doors are 36” wide, whether in a house or commercial building
  You will find smaller doors in houses, especially closet, bathrooms, etc., but 36” is very standard
  Doors should always be represented with a line for the door and arc for the door swing
  This is extremely important as it matters greatly which way a door swings

## Slide 9: Creating Floor Plans - Windows
  Windows come in all shapes and sizes
  There is not always a window within a room, but typically there is at least one
  Window symbols can vary greatly depending on the style of window, but typically a “double-hung” type of window is used to show the location of a window
  This is represent with two close parallel lines in the center of the wall
  Depending on the type, the window sill and other amenities could also be indicated

## Slide 10: Creating Floor Plans - Dimensions
  Are a way to represent measurements on a drawing
  They are usually placed from one side to the other around the outside of the drawing geometry
  After this, the inside dimensions are placed to indicate anything not covered by the outside dimensions
  It is best practice to show the least amount of dimensions possible while accurately giving all measurements
  Properly dimensioning a drawing takes skill and knowledge, over time, it becomes easier to master this art

## Slide 11: Work Time!
  Let’s apply your new found knowledge and sketch out a room