## Slide 1
Flexible Manufacturing
  Blueprints in Manufacturing

## Slide 3: How to Read Blueprints
1/2” ROUND STOCK
3
1/4-20 THREADS 3/4” DEEP
HAMMER HANDLE
6
1/4” ROUND STOCK
1/4-20 THREADS X 3/4 LENGTH BOTH ENDS
HAMMER SHANK
3/4 SQUARE STOCK
2 1/2
1 1/8
1
3/8
1/4-20 THREADS
3/4” DEEP
HAMMER HEAD
1/8

## Slide 4: How to Read Blueprints
  Describe the part to be made; show dimension, location, material, and finished part
2 ½
2 ½
2 ⅞
7 ½
1 ½
¾
¼
3
2 Dia.
⅞
2 ⅞
½ DRILL
2 HOLES
⅞ DRILL
3

## Slide 5: How to Read Blueprints
  Dimensions show the total size of the part.
  The outside dimension is usually the total size.
  The support would need to be machined from a piece
  5¾” X 2½” X 3”.
2 ½
2 ½
2 ⅞
7 ½
1 ½
¾
¼
3
2 Dia.
⅞
2 ⅞
½ DRILL
2 HOLES
⅞ DRILL
3

## Slide 6: How to Read Blueprints
  The two ½” holes are drilled 1 ½” from the edge and 2 ⅞” from the center line of the part.
2 ½
2 ½
2 ⅞
7 ½
1 ½
¾
¼
3
2 Dia.
⅞
2 ⅞
½ DRILL
2 HOLES
⅞ DRILL
3
  Locations are for machining the part to shape or for locating placement of other features.

## Slide 7: Hammer Handle
  What is the diameter of the round stock used to make the handle?
  What is the length of the material?
  What is the size of the threads in the end?
1/2” ROUND STOCK
3
1/4-20 THREADS 3/4” DEEP

## Slide 8: Hammer Handle
  What is the diameter of the round stock used to make the handle? 1/2”
  What is the length of the material? 3”
  What is the size of the threads in the end?
  1/4”- 20 threads and 3/4” deep
1/2” ROUND STOCK
3
1/4-20 THREADS 3/4” DEEP

## Slide 9: Hammer Head
  What is the stock size for the head?
  What is the length of the head?
  What is the measurement for the placement of the hole?
3/4 SQUARE STOCK
2 1/2
1 1/8
1
3/8
1/4-20 THREADS
3/4” DEEP
1/8

## Slide 10: Hammer Head
  What is the stock size for the head?
  3/4” square stock
  What is the length of the head?
  1/2”
  What is the measurement for the placement of the hole?
1-1/8” up and 3/8” in from the side
3/4 SQUARE STOCK
2 1/2
1 1/8
1
3/8
1/4-20 THREADS
3/4” DEEP
1/8

## Slide 11: Lines Used in a Blueprint
Line | Name | Explanation
 | Object | Dark heavy line that denotes the edge of an object.
 | Hidden | Dark heavy dash that denotes an edge behind or inside the object.
 | Center | A line that is thinner than an object line with a dash in the center of the line to denote the center of the part or circle.
 | Extension | A thin line extending an edge from the object for dimensions to touch.
 | Dimension | A set of arrows pointing to the extension line with a dimension in the middle.
 | Cutting Plan | The heaviest line on a drawing showing where a section is to be cut out of the object.
 | Section | Thin lines at a diagonal showing the cut portion of an object.
 | Leader | A straight line with an arrow extending from it to point to a dimension or note.

## Slide 12: Screw Jack Base Plans
Extension line
Dimension line
Center line
Section line
Cutting plane line
Object line
Notes
Leader line
Hidden line

## Slide 13: Identify the Type of Lines
0.25
0.375
0.75
2.50
1.00
DRILL #3 BIT X.50 DEEP,
TAP TO 1/4 – 28 THREAD SIZE
1.25
0.375
1.50
0.50
DRILL TWO,
0.25 HOLES
2.00
0.75
0.50
0.75
0.25
BORE 0.50 DIA. X 0.375 DEEP HOLE
1.00
#8 – 32 SETSCREW
DRILL #29 (0.136) HOLE
A.
B.
C.
D.
E.
F.

## Slide 14: Identify the Type of Lines
0.25
0.375
0.75
2.50
1.00
DRILL #3 BIT X .50 DEEP,
TAP TO 1/4 – 28 THREAD SIZE
1.25
0.375
1.50
0.50
DRILL TWO,
0.25 HOLES
2.00
0.75
0.50
0.75
0.25
BORE 0.50 DIA. X 0.375 DEEP HOLE
1.00
#8 – 32 SETSCREW
DRILL #29 (0.136) HOLE
Object
Leader
Dimension
Centerline
Hidden
Extension

## Slide 15: Metal sizes needed to make the cooker base

## Slide 16: Handout for Blueprint Reading

## Slide 17: Handout for Blueprint Reading
  What sized piece of aluminum will be needed to machine the cap?
  What size and how deep is the hole drilled in the bottom?

## Slide 18: Handout for Blueprint Reading
  What sized piece of aluminum will be needed to machine the cap?
  3/4” diameter X 3/4” long
  What size and how deep is the hole drilled in the bottom?
  0.375 Drill X 0.500” Deep

## Slide 19: Using Charts
Vise Bill of Materials |  |  | 
PART NUMBER | QUANITY | NAME | SIZE
1 | 1 | BASE | ¾ X 2 ½ X 5
2 | 1 | FIX JAW | ¾ X 2 ½ X 2
3 | 1 | MOVABLE JAW | ¾ X 2 ½ X 2
4 | 1 | FRONT JAW | ¾ X 2 ½ X 2
5 | 1 | SCREW | 1 ¼ DIA X 3 ¾
6 | 1 | HANDLE | ⅜ DIA X 3
7 | 2 | JAW FACES | ½ X 1 X 2 ½
8 | 1 | JAW LOCK | ⅛ X ¾ X 1 ½
9 | 7 | FASTENER | ¼ – 28 BOLTS X ¾ LONG
10 | 1 | SETSCREW (NOT SHOWN) | ⅛ SETSCREW X ¾ LONG
19

## Slide 20: Charts
  List information in table form.
  There are different types of charts: Bill of Materials, Tap Sizes, Drill Sizes, and Feed and Cut Rates.
  The Bill of Materials will give you part sizes, types of material, and finishes for all the different parts.
  The other charts give information on sizes needed to make a part or standards used in the manufacturing.
PART NUMBER | QUANITY | NAME | SIZE
1 | 1 | BASE | ¾ X 2 ½ X 5
2 | 1 | FIX JAW | ¾ X2 ½ X2
3 | 1 | MOVABLE JAW | ¾ X2 ½ X2
4 | 1 | FRONT JAW | ¾ X2 ½ X2
5 | 1 | SCREW | 1 ¼ DIA X 3 ¾
6 | 1 | HANDLE | ⅜ DIA X 3
7 | 2 | JAW FACES | ½ X 1 X 2 ½
8 | 1 | JAW LOCK | ⅛ X ¾ X 1 ½
9 | 7 | FASTNER | ¼ –28 BOLTS X ¾ LONG
10 | 1 | SETSCREW (NOT SHOWN) | ⅛ SETSCREW X ¾ LONG
Thread Size | Drill Size | Decimal Equivalent | National
¼ - 20 | #7 | 0.2010 | Course
¼ -28 | #3 | 0.230 | Fine
5/16 - 18 | F | 0.2570 | Course
5/16 - 24 | I | 0.2720 | Fine
3/8 -16 | 5/16 | 0.3125 | Course
3/8 - 24 | Q | 0.3320 | Fine
7/16 - 14 | U | 0.3320 | Course
7/16 - 20 | 25/64 | 0.3906 | Fine
½ - 13 | 27/64 | 0.4219 | Course
½ - 20 | 29/64 | 0.4531 | Fine

## Slide 21: Exploded View of Vise Parts
  The Bill of Materials is filled out about each part.
1
7
4
3
2
9
8
6
5

## Slide 22: Vise Bill of Materials
PART NUMBER | QUANITY | NAME | SIZE
1 | 1 | BASE | ¾ X 2 ½ X 5
2 | 1 | FIX JAW | ¾ X 2 ½ X 2
3 | 1 | MOVABLE JAW | ¾ X 2 ½ X 2
4 | 1 | FRONT JAW | ¾ X 2 ½ X 2
5 | 1 | SCREW | 1 ¼ DIA X 3 ¾
6 | 1 | HANDLE | ⅜ DIA X 3
7 | 2 | JAW FACES | ½ X 1 X 2 ½
8 | 1 | JAW LOCK | ⅛ X ¾ X 1 ½
9 | 7 | FASTENER | ¼ – 28 BOLTS X ¾ LONG
10 | 1 | SETSCREW (NOT SHOWN) | ⅛ SETSCREW X ¾ LONG

## Slide 23: Fill in the Bill of Material for the Base
SCREW JACK PARTS LIST |  |  |  | 
NAME | MATERIAL | LENGTH | DIAMETER | FINISH
BASE | ? | ? | ? | ?