## Slide 1
Flexible Manufacturing
  Just-In-Time Manufacturing

## Slide 3: Just-in-Time Manufacturing
Just-in-Time (JIT) manufacturing is a system of manufacturing where a company will purchase materials and produce a product when a customer orders that product.

## Slide 4: Just-in-Time Manufacturing
The system works by having materials and parts delivered on an “as needed” basis. The materials that are needed are delivered directly to the assembly line.

## Slide 5: Just-in-Time Manufacturing
This system of manufacturing has the customer in control of the rate of production. If a customer wants a standard supply of a product, the manufacturer can use this method to keep just enough products on hand to fill that order.

## Slide 6: Just-in-Time Manufacturing
The use of Just-in-Time manufacturing has brought the cost of manufacturing down. The cost of large supplies of raw material is reduced and the cost of stocking finished products is also reduced.

## Slide 7: Just-in-Time Manufacturing
The companies that use Just-in-Time manufacturing enable the workers to do more than just run a piece of equipment. The worker can make suggestions for improvement, check for quality, and are encouraged to learn more operations in the manufacturing operation.

## Slide 8: Just-in-Time Manufacturing
A system of cards are used to keep track of the parts needed, or parts that are in production. These cards are called “kanban.”

## Slide 9: Kanban
  Means “signboard” in Japanese
  In Just-in-Time manufacturing, it is a card or sign used to track products and supplies.
Flexible Manufacturing Lab | 
Standard Bolt | 
¼” -20 Threads | 
200 | 20
$0.04 | Supply cabinet #2

## Slide 10: Kanban
  The card tells the product name, size, number to order, price, safe stock, and storage area.
  The card shown here has a picture of the product included.
Flexible Manufacturing Lab | 
Standard Bolt | 
¼” -20 Threads | 
200 | 20
$0.04 | Supply Cabinet #2
Part Name
Storage Location
Size
Number to Reorder
Safe Stock
Photo
Price

## Slide 11: Use of the Kanban
  The card will be in or on the storage container. When the items in the container are used to the point of the “safe stock” (20 bolts) the product is restocked in the amount listed (200 bolts)
Flexible Manufacturing Lab | 
Standard Bolt | 
¼” -20 Threads | 
200 | 20
$0.04 | Supply Cabinet #2

## Slide 12: Where did the number come from?
  The safe number is the amount of the item needed to be on hand until a new order can be received
  The numbers are monitored to keep the supply correct, so the line will not stop production
Flexible Manufacturing Lab | 
Standard Bolt | 
¼” -20 Threads | 
200 | 20
$0.04 | Supply Cabinet #2

## Slide 13: Where did the number come from?
  The reorder number is the amount of product that will be used over a given time, one day, or one production cycle.
  The numbers are monitored to keep the supply correct, so the line will not stop production.
Flexible Manufacturing Lab | 
Standard Bolt | 
¼” -20 Threads | 
200 | 20
$0.04 | Supply Cabinet #2

## Slide 14: Just-in-Time in A Flexible Lab
  The use of the “kanban” card can keep supplies organized and in stock.
  The sheet metal box is set up for a simple mass production project.
  The box has three parts:
    A box,
    a lid, and
    two pop rivets as hinges.
Notes: The vise project could be developed into a mass production project and use the system.

## Slide 15: Sheet Metal Box

## Slide 16: Box Plans
Box Bottom
Box Top

## Slide 17
Box Bottom

## Slide 18
Box Top

## Slide 19
SHEET METAL BOX |  |  |  |  |  | 
BILL OF MATERIALS |  |  |  |  |  | 
NAME | Quality | MATERIAL | THICKNESS | WIDTH | LENGTH | FINISH
BOX | 1 | SHEET METAL | 24 GAUGE | 6¾ | 12¾ | PAINTED
LID | 1 | SHEET METAL | 24 GAUGE | 5 ¹³/₁₆ | 12 ¹³/₁₆ | PAINTED
POP RIVITS | 2 | METAL | ⅛ DIAMETER |  | ⅛” Long | 

## Slide 20: Box Kanbans
Flexible Manufacturing Lab | 
Box | 
24 Gauge Sheet Metal | 
30 | 5
$0.95 | Supply Cabinet #1
Flexible Manufacturing Lab | 
Box Lid | 
24 Gauge Sheet Metal | 
30 | 5
$0.75 | Supply Cabinet #1
Flexible Manufacturing Lab | 
Pop Rivets | 
⅛ Diameter x ⅛ Long | 
70 | 10
$0.06 | Supply Cabinet #2

## Slide 21: Box Bottom
Manufacturing Operations | 
Operation Name | Tool or Equipment
Design layout | Sheet metal bluing, scribe, and ruler
Cutting bottom shape | Aviation tin snips
Fold long sides hems | Box and pan brake
Fold short sides to 90° | Box and pan brake
Fold long sides to 90° | Box and pan brake
Fold short side hems | Box and pan brake
Put in storage until assembly operation | Storage area

## Slide 22: Box Top
Manufacturing Operations | 
Operation Name | Tool or Equipment
Design layout | Sheet metal bluing, scribe and ruler
Cutting bottom shape | Aviation tin snips
Fold long sides hems | Box and pan brake
Fold short sides to 90° | Box and pan brake
Fold long sides to 90° | Box and pan brake
Fold short side hems | Box and pan brake
Put in storage until assembly operation | Storage area

## Slide 23: Box Assemble
Manufacturing Operations | 
Operation Name | Tool or Equipment
Layout hinge holes on lid | Sheet metal bluing, scribe, and ruler
Drilling or punch hinge holes | Hand drill, ⅛ bit, and backer board
Place lid on the box bottom | 
Drilling hinge holes in the box bottom | Hand drill, ⅛ bit, and backer board
Install pop rivets | Pop rivet tool
Paint box | Spray can of paint
Put in storage until grading time | Storage area

## Slide 24: Resources
  Wright, R. T. (2004). Manufacturing and automation technology. Engineering Manufacturing Facilities (22, pp. 300-301). Tinley Park, IL: Goodheart-Wilcox.
  Wright, R. T. (2004). Manufacturing and automation technology. Computer Systems in Product Manufacturing (36, pp. 433-434). Tinley Park, IL: Goodheart-Wilcox.